XCAT 2 on AIX
Booting AIX diskless nodes
2010／11／19, AM 10:12:01

# Overview
This “How-To” describes how AIX diskless nodes can be deployed and updated using xCAT and AIX/NIM commands.
NIM (Network Installation Management) is an AIX tool that enables a cluster administrator to centrally manage the installation and configuration of AIX and optional software on machines within a networked environment. This document assumes you are somewhat familiar with NIM. For more information about NIM, see the IBM AIX Installation Guide and Reference. (http://www-03.ibm.com/servers/aix/library/index.html)
The process described below is one basic set of steps that may be used to boot AIX diskless nodes and is not meant to be a comprehensive guide of all the available xCAT or NIM options.
Before starting this process it is assumed you have completed the following.
- An AIX system has been installed to use as an xCAT management node.
- xCAT and prerequisite software has been installed on the management node.
- The xCAT management node has been configured.
- One or more LPARs have already been created using the HMC interfaces.
- The cluster management network has been set up. (The Ethernet network that will be used to do the network installation of the cluster nodes.)
# Deploying AIX diskless nodes using xCAT
## Create a diskless image
In order to boot a diskless AIX node using xCAT and NIM you must create an xCAT osimage definition as well as several NIM resources.
The mknimimage will handle all the NIM setup as well as the creation of the xCAT osimage definition. It will not attempt to reinstall or reconfigure NIM if that process has already been completed. See the mknimimage man page for additional details.
Note: For various reasons it is recommended that you make sure that the primary hostname of the management node is the interface that you will be using to install the nodes. If you do this before you configure NIM then NIM will automatically use it to define the NIM primary network. This will mean that you will not have to create any additional NIM network definitions and could avoid additional complications.
If you wish to install and configure NIM manually you can run the AIX nim_master_setup command (Ex. “nim_master_setup -a mk_resource=no -a device=<source directory>").
By default, the mknimimage command will create the NIM resources in subdirectories of /install. Some of the NIM resources are quite large (1-2G) so it may be necessary to increase the files size limit.
For example, to set the file size limit to “unlimited” for the user “root” you could run the following command.
/usr/bin/chuser fsize=-1 root
There are several NIM resources that must be created in order to deploy a diskless node. The main resource is the NIM SPOT (Shared Product Object Tree). An AIX diskless image is essentially a SPOT. It provides a /usr file system for diskless nodes and a root directory whose contents will be used for the initial diskless nodes root directory. It also provides network boot support.
When you run the command you must provide a source for the installable images. This could be the AIX product media, a directory containing the AIX images, or the name of an existing NIM lpp_source resource. You must also provide a name for the osimage you wish to create. This name will be used for the NIM SPOT resource that is created as well as the name of the xCAT osimage definition. The naming convention for the other NIM resources that are created is the osimage name followed by the NIM resource type, (ex. “ 61cosi_lpp_source”).
Stateful or stateless?
You can choose to have your diskless nodes be either “stateful” or “stateless”. If you want a “stateful” node you must use a NIM “root” resource. If you want a “stateless” node you must use a NIM “shared_root” resource.
A “stateful” diskless node preserves its state in individual mounted root filesystems. When the node is shut down and rebooted, any information that was written to a root filesystem will be available
A “stateless “ diskless node uses a mounted root filesystem that is shared with other nodes. When it writes to the root directory the information is actually written to memory. If the node is shut down and rebooted any data that was written is lost. Any node-specific information must be re-established when the node is booted.
The advantage of stateless nodes is that there is much less network traffic and fewer resources used which is especially important in a large cluster environment.
For more information regarding the NIM “root” and “shared_root” resource refer to the NIM documentation.
If you wish to set up stateless cluster nodes you must use the “-r” option when you run the mknimimage command. The default behavior would be to set up stateful nodes.
For example, to create a stateless-diskless osimage called “61cosi” using the software contained in the /myimages directory you could issue the following command.
mknimimage -V -r -t diskless -s /myimages 61cosi
(Note that this operation could take a while to complete!)
Caution: Do not interrupt (kill) a NIM process while it is creating a SPOT resource.
Starting with xCAT version 2.5 you can also use the “-D” option to specify that a dump resource should be created. See the section called “ISCSI dump support” below for details.
Note: To populate the /myimages directory you could copy the software from the AIX product media using the AIX gencopy command. For example you could run “gencopy -U -X -d /dev/cd0 -t /myimages all".
The mknimimage command will display a summary of what was created when it completes. For example:
Object name: 61cosi
    imagetype=NIM
    lpp_source=61cosi_lpp_source
    nimtype=diskless
    osname=AIX
    paging=61cosi_paging
    shared_root=61cosi_shared_root
    spot=61cosi

The NIM resources will be created in a subdirectory of /install/nim by default. You can use the “-l” option to specify a different location.
You can also specify alternate or additional resources on the command line using the “attr=value” option, (“<nim resource type>=<resource name>”). For example, if you want to include a “resolv_conf” resource named “61cosi_resolv_conf” you could run the command as follows.
mknimimage -V -r -t diskless -s /myimages 61cosi resolv_conf=61cosi_resolv_conf
Any additional NIM resources specified on the command line must be previously created using NIM interfaces. (Which means NIM must already have been configured previously. )
Note: Another alternative is to run mknimimage without the additional resources and then simply add them to the xCAT osimage definition later. You can add or change the osimage definition at any time. When you initialize and install the nodes xCAT will use whatever resources are specified in the osimage definition.
The xCAT osimage definition can be listed using the lsdef command, modified using the chdef command and removed using the rmnimimage command. See the man pages for details.
To get details for the NIM resource definitions use the AIX lsnim command. For example, if the name of your SPOT resource is "61cosi" then you could get the details by running:
lsnim -l 61cosi
To see the actual contents of a NIM resource use "nim -o showres <resource name>". For example, to get a list of the software installed in your SPOT you could run:
        nim -o showres 61cosi
## Update the image (SPOT)

You must install any additional software you need and make any required customizations to the image before you boot the nodes.
### Update options
There are basically three types of updates you can do to a SPOT.
#### Add or update software
The SPOT created in the previous step should be considered the basic minimal diskless AIX operating system image. It does not contain all the software that would normally be installed as part of AIX, if you were installing a standalone system from the AIX product media. (The “nim -o showres ...” command mentioned above will display what software is contained in the SPOT.)
You can use the mknimimage “-u” option to update software in the diskless image (SPOT).
To do this you can update your xCAT osimage definition with any “installp_bundles”, “otherpkgs” you wish to use and then run the mknimimage -u command.
Use the chdef command to update the osimage definition. For example:
chdef -t osimage -o 61cosi installp_bundle=”hpcbnd,labbnd”
Once the osimage definition is updated you can run mknimimage.
mknimimage -u 61cosi
Note: You can also specify “installp_bundle” and “otherpkgs” on the command line. However in this case you wouldn't have a record of what software was added to the SPOT.
#### Update system configuration files.

You can also add other configuration files such as /etc/passwd etc. These files will then be available to every node that boots with this image.
This can be done manually or by setting the “synclists” attribute of the osimage definition to point to a synclists file. This file contains a list of configuration files etc. that you wish to have copied into the SPOT.
For more information on using the synchronization file function see the document called “How to sync files in xCAT” ( http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2SyncFilesHowTo.pdf )
Use the chdef command to update the osimage definition. For example:
chdef -t osimage -o 61cosi synclists=”/u/test/mysyncfiles”
Once the osimage definition is updated you can run mknimimage.
mknimimage -u 61cosi
Note: You can do BOTH the software updates and configuration file updates at the same time with one call to mknimimage.

#### Run commands in the SPOT using chroot.
Starting with xCAT 2.5 and AIX 6.1.6 the xcatchroot command can be used to modify the SPOT using the chroot command.
The xcatchroot command will take care of any of the required setup so that the command you provide will be able to run in the spot chroot environment. It will also mount the lpp_source resource listed in the osimage definition so that you can access additional software that you may wish to install.
For example, to set the root password to "cluster" in the spot so that when the diskless node boots it will have a root password set you could run a command similar to the following.
xcatchroot -i 61cosi "/usr/bin/echo root:cluster | /usr/bin/chpasswd -c"
See the xcatchroot man page for more details.
Caution:
Be very careful when using chroot on a SPOT. It is easy to get the SPOT into an unusable state! It may be adviseable to make a copy of the SPOT before you try to run any commands that have an uncertain outcome.
When you are done updating a NIM spot resource you should always run the NIM check operation on the spot.
nim -Fo check 61cosi
For more information on updating a diskless image see the document called “Updating AIX cluster nodes” (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIXUpdates.pdf)
See the section titled “Updating diskless nodes”
### Adding required software

You will have to install openssl and openssh along with several additional requisite software packages.
The basic process is:
- Copy the required software to the lpp_source resource that you used to create your SPOT.
- Create NIM installp_bundle resources
- Check the lpp_source and bundle files
- Install the software in the SPOT.
#### Copy the software.
You will have to update the SPOT with additional software required for xCAT.
The required software is specified in the sample bundle file discussed below. The installp filesets should be available from the AIX product media. The prerequisite rpms are available in the dep-aix-<version>.tar.gz tar file that you downloaded from the xCAT download page.
The required software must be copied to the NIM lpp_source resource that is being used for this OS image. The easiest way to do this is to use the “nim -o update” command.
For example, assume the dep-aix* .tar.gz file has been copied and unwrapped in the /tmp/images directory and that the name of the NIM lpp_source resource is “61cosi_lpp_source”.
In more recent versions of the dep-aix* tar file the software will be found in subdirectories corresponding to the level of AIX you are using. (ex. ./dep-aix/5.3, ./dep-aix/6.1).
Note: Typically all the rpms are copied to the lpp_source resource even though they are not all used when installing a compute node.
For example, to copy all the rpms from the dep-aix package you could run the following command.
nim -o update -a packages=all -a source=/tmp/images/dep-aix/6.1	61cosi_lpp_source
The NIM command will find the correct directories and update the lpp_source resource.
#### Create NIM installp_bundle resources
To get all this additional software installed we need a way to tell NIM to include it in the installation. To facilitate this, xCAT provides sample NIM installp bundle files. (Always make sure that the contents of the bundle files you use are the packages you want to install and that they are all in the appropriate lpp_source directory.)
Starting with xCAT version 2.4.3 there will be a set of bundle files to use for installing a compute node. They are in “/opt/xcat/share/xcat/installp_bundles”. There is a version corresponding to the different AIX OS levels. (xCATaixCN53.bnd, xCATaixCN61.bnd etc.) Just use the one that corresponds to the version of AIX you are running.
Note: For earlier versions of xCAT the sample bundle files are shipped as part of the xCAT tarball file.
To use the bundle file you need to define it as a NIM resources and add it to the xCAT osimage definition.
Copy the bundle file ( say xCATaixCN61.bnd ) to a location where it can be defined as a NIM resource, for example “/install/nim/installp_bundle”.
To define the NIM resource you can run the following command.
nim -o define -t installp_bundle -a server=master -a location=	/install/nim/installp_bundle/xCATaixCN61.bnd xCATaixCN61
To add this bundle resource to your xCAT osimage definition run:
chdef -t osimage -o 610SNimage installp_bundle=”xCATaixSN61”
#### Check the osimage (optional)

This command is available in xCAT 2.4.3 and beyond.

To avoid potential problems when installing a node it is adviseable to verify that all the software that you wish to install has been copied to the appropriate NIM lpp_source directory.
Any software that is specified in the “otherpkgs” or the “installp_bundle” attributes of the osimage definition must be available in the lpp_source directories.
Also, if your bundle files include rpm entries that use a wildcard (*) you must make sure the lpp_source directory does not contain multiple packages that will match that entry. (NIM will attempt to install multiple version of the same package and produce an error!)
To find the location of the lpp_source directories run the “lsnim -l <lpp_source_name>” command. For example:
lsnim -l 610image_lpp_source
If the location of your lpp_source resource is "/install/nim/lpp_source/610image_lpp_source/" then you would find rpm packages in "/install/nim/lpp_source/610image_lpp_source/RPMS/ppc" and you would find your installp and emgr packages in "/install/nim/lpp_source/610image_lpp_source/installp/ppc".
To find the location of the installp_bundle resource files you can use the NIM “lsnim -l” command. For example,
lsnim -l xCATaixSSH
Starting with xCAT version 2.4.3 you can use the xCAT chkosimage command to do this checking. For example:
chkosimage -V 61cosi
See the chkosimage man page for details.
#### Install the software into the SPOT.
You can install and update software in a NIM SPOT resource by using NIM commands directly or you can use the xCAT mknimimage command.
If you wish to use the NIM support directly you can check the NIM documentation for information on the NIM “cust” and “maint” operations.
In this example the xCAT mknimimage command will be used.
Run the mknimimage command to update the SPOT using the information saved in the xCAT "61cosi" osimage definition.
mknimimage -u 61cosi
See the mknimimage man page for more options that are available for updating diskless images (SPOT resources).
Once you are done updating the SPOT you must always run the NIM “check” operation.
nim -o check 61cosi
Note: You cannot update a SPOT that is currently allocated. To check to see if the SPOT is allocated you could run the following command.
lsnim -l <spot name>

### Set up statelite support (for diskless-stateless nodes only)

This support is available in xCAT version 2.5 and beyond.

The xCAT statelite support for AIX provides the ability to “overlay” specific files or directories over the standard diskless-stateless support.

There is a complete description of the statelite support in (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIX.pdf).
See the section titled “Using AIX statelite support”.
To set up the statelite support you must:
1. fill in one or more to the statelite tables in the xCAT database.
2. Run the “mknimimage -u” command which will use that information to modify the SPOT resource.
Note: You could also fill in the statelite tables before initially running the mknimimage to create the osimage. (Rather than doing the setup later with the “-u” option.)
## Define xCAT networks
Create a network definition for each network that contains cluster nodes. You will need a name for the network and values for the following attributes.
net The network address.
mask The network mask.
gateway The network gateway.

This “How-To” assumes that all the cluster node management interfaces and the xCAT management node interface are on the same network. You can use the xCAT mkdef command to define the network.

For example:

mkdef -t network -o net1 net=9.114.113.0 mask=255.255.255.224	gateway=9.114.113.254

  Note: NIM also requires network definitions. When NIM was configured in an earlier step the default NIM master network definition was created. The NIM definition should match the one you create for xCAT. If multiple cluster subnets are needed then you will need an xCAT and NIM network definition for each one. A future xCAT enhancement will simplify this by automatically creating NIM network definitions based on the xCAT definitions.

## Create additional NIM network definitions (optional)

For the processs described in this document we are assuming that the xCAT management node and the LPARs are all on the same network.
However, depending on your specific situation, you may need to create additional NIM network and route definitions.
NIM network definitions represent the networks used in the NIM environment. When you configure NIM, the primary network associated with the NIM master is automatically defined. You need to define additional networks only if there are nodes that reside on other local area networks or subnets. If the physical network is changed in any way, the NIM network definitions need to be modified.
To create the NIM network definitions corresponding to the xCAT network definitions you can use the xCAT xcat2nim command.
For example, to create the NIM definitions corresponding to the xCAT “clstr_net” network you could run the following command.
xcat2nim -V -t network -o clstr_net
Manual method
The following is an example of how to define a new NIM network using the NIM command line interface.
Step 1
Create a NIM network definition. Assume the NIM name for the new network is “clstr_net”, the network address is “10.0.0.0”, the network mask is “255.0.0.0”, and the default gateway is “10.0.0.247”.
nim -o define -t ent -a net_addr=10.0.0.0 -a snm=255.0.0.0 -a	routing1='default 10.0.0.247' clstr_net
Step 2
Create a new interface entry for the NIM “master” definition. Assume that the next available interface index is “2” and the hostname of the NIM master is “xcataixmn”. This must be the hostname of the management node interface that is connected to the “clstr_net” network.
nim -o change -a if2='clstr_net xcataixmn 0' -a cable_type2=N/A master
Step 3
Create routing information so that NIM knows how to get from one network to the other. Assume the next available routing index is “2”, and the IP address of the NIM master on the “master_net” network is “8.124.37.24”. Assume the IP address on the NIM master on the “clstr_net” network is “ 10.0.0.241”. This command will set the route from “master_net” to “clstr_net” to be “ 10.0.0.241” and it will set the route from “clstr_net” to “master_net” to be “8.124.37.24”.
nim -o change -a routing2='master_net 10.0.0.241 8.124.37.24'	clstr_net
Step 4
Verify the definitions by running the following commands.
lsnim -l master
lsnim -l master_net
lsnim -l clstr_net

See the NIM documentation for details on creating additional network and route definitions. (IBM AIX Installation Guide and Reference. http://www-03.ibm.com/servers/aix/library/index.html)
## Define the HMC as an xCAT node
The xCAT hardware control support requires that the hardware control point for the nodes also be defined as a cluster node.
The following command will create an xCAT node definition for an HMC with a host name of “hmc01”. The groups, nodetype, mgt, username, and password attributes must be set.
mkdef –t node –o hmc01 groups=”all” nodetype=hmc mgt=hmc	username=hscroot password=def456
## Discover the LPARs managed by the HMC
This step assumes that the LPARs were already created using the standard HMC interfaces.
Use the xCAT rscan command to gather the LPAR information. In this example we will use the “-z” option to create a stanza file that contains the information gathered by rscan as well as some default values that could be used for the node definitions.
To write the stanza format output of rscan to a file called “mystanzafile” run the following command.
rscan –z hmc01 > mystanzafile
This file can then be checked and modified as needed. For example you may need to add a different name for the node definition or add additional attributes and values etc.
Note: The stanza file will contain stanzas for objects other than the LPARs. This information must also be defined in the xCAT database. It is not necessary to modify the non-LPAR stanzas in any way.
## Define xCAT cluster nodes
The information gathered by the rscan command can be used to create xCAT node definitions.
Since we have put all the node information in a stanza file we can now pass the contents of the file to the mkdef command to add the definitions to the database.
cat mystanzafile | mkdef –z
You can use the xCAT lsdef command to check the definitions (ex. “lsdef –l node01”). After the node has been defined you can use the chdef command to make any additional updates to the definitions, if needed.
## Add IP addresses and hostnames to /etc/hosts

Make sure all node hostnames are added to /etc/hosts. Refer to the section titled “Add cluster nodes to the /etc/hosts file” in the following document for details. (http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2onAIX.pdf)

## Create and define additional logical partitions (optional)

You can use the xCAT mkvm command to create additional logical partitions for diskless nodes in some cases.

This command can be used to create new partitions based on an existing partition or it can replicate the partitions from a source CEC to a destination CEC.

The first form of the mkvm command creates new partition(s) with the same profile/resources as the partition specified on the command line. The starting numeric partition number and the noderange for the newly created partitions must also be provided. The LHEA port numbers and the HCA index numbers will be automatically increased if they are defined in the source partition.

The second form of this command duplicates all the partitions from the specified source CEC to the destination CEC. The source and destination CECs can be managed by different HMCs.

The nodes in the noderange must already be defined in the xCAT database. The “mgt” attribute of the node definitions must be set to “hmc”.

For example, to create a set of new nodes. (The “groups” attribute is required.)

mkdef -t node -o clstrn04-clstrn10 groups=all,aixnodes mgt=hmc

To create several new partitions based on the partition for node clstrn01.

mkvm -V clstn01 -i 4 -n clstrn04-clstrn10

See the mkvm man page for more details.
## Gather MAC information for the boot adapters.
Use the xCAT getmacs command to gather adapter information from the nodes. This command will return the MAC information for each Ethernet adapter available on the target node. The command can be used to either display the results or write the information directly to the database. If there are multiple adapters the first one will be written to the database and used as the install adapter for that node.
The command can also be used to do a ping test on the adapter interfaces to determine which ones could be used to perform the network boot. In this case the first adapter that can be successfully used to ping the server will be written to the database.
Before running getmacs you must first run the makeconservercf command. You need to run makeconservercf any time you add new nodes to the cluster.
makeconservercf
To retrieve the MAC address for all the nodes in the group “aixnodes” and write the first adapter MAC to the xCAT database you could issue the following command.
getmacs aixnodes
To display all adapter information but not write anything to the database.
getmacs -d aixnodes
To retrieve the MAC address and do a ping test to determine which adapter MAC to use for the node you could issue the following command. (The ping operation may take a while to complete.)
getmacs -d aixnodes -S 10.14.0.2 -G 10.14.0.2 -C 10.14.0.4
The output would be similar to the following.
# Type Location Code MAC Address Full Path Name Ping Result Device Type
ent U9125.F2A.024C362-V6-C2-T1 fef9dfb7c602 /vdevice/l-lan@30000002 successful virtual
ent U9125.F2A.024C362-V6-C3-T1 fef9dfb7c603 /vdevice/l-lan@30000003 unsuccessful virtual
From this result you can see that “ fef9dfb7c602” should be used for this nodes MAC address.
For more information on using the getmacs command see the man page.
To manually add a MAC value to the node definition you can use the chdef command. For example:
chdef -t node node01 mac=fef9dfb7c603
## Define xCAT groups (optional)
XCAT supports both static and dynamic node groups. See the section titled “xCAT node group support” in the “xCAT2 Top Doc” document for details on using xCAT groups. ( http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2top.pdf)

## Set up post boot scripts (optional)

xCAT supports the running of customization scripts on the nodes when they are installed. For diskless nodes these scripts are run when the /etc/inittab file is processed during the node boot up.
This support includes:
- The running of a set of default customization scripts that are required by xCAT.
  You can see what scripts xCAT will run by default by looking at the “xcatdefaults” entry in the xCAT “postscripts” database table. ( I.e. Run “tabdump postscripts”.). You can change the default setting by using the xCAT chtab or tabedit command. The scripts are contained in the /install/postscripts directory on the xCAT management node.
- The optional running of customization scripts provided by xCAT.
  There is a set of xCAT customization scripts provided in the /install/postscripts directory that can be used to perform optional tasks such as additional adapter configuration. (See the “configiba” script for example.)
- The optional running of user-provided customization scripts.
To have your script run on the nodes:
1. Put a copy of your script in /install/postscripts on the xCAT management node. (Make sure it is executable.)
2. Set the “postscripts” attribute of the node definition to include the comma separated list of the scripts that you want to be executed on the nodes. The order of the scripts in the list determines the order in which they will be run. For example, if you want to have your two scripts called “foo” and “bar” run on node “node01” you could use the chdef command as follows.
chdef -t node -o node01 -p postscripts=foo,bar
(The “-p” means to add these to whatever is already set.)
Note: The customization scripts are run during the boot process (out of /etc/inittab).
## Set up prescripts (optional)

This support will be available in xCAT 2.5 and beyond.

The xCAT prescript support is provided to to run user-provided scripts during the node initialization process. These scripts can be used to help set up specific environments on the servers that handle the cluster node deployment. The scripts will run on the install server for the nodes. (Either the management node or a service node.) A different set of scripts may be specified for each node if desired.

One or more user-provided prescripts may be specified to be run either at the beginning or the end of node initialization. The node initialization on AIX is done either by the nimnodeset command (for diskfull nodes) or the mkdsklsnode command (for diskless nodes.)

For more information about using the xCAT prescript support refer to the des cription earlier in this documant and also the “xCAT2 Top Doc”, ( http://xcat.svn.sourceforge.net/viewvc/xcat/xcat-core/trunk/xCAT-client/share/doc/xCAT2top.pdf)
## Verify the node definitions
Verify that the node definitions include the required information.
To get a listing of the node definitions you can use the lsdef command. For example, to display the definitions of all nodes in the group “aixnodes” you could run the following command.
lsdef -t node -l -o aixnodes
The output for one diskless node might look something like the following:
Object name: clstrn02
    cons=hmc
    groups=lpar,all
    hcp=clstrhmc01
    hostnames=clstrn02.mycluster.com
    id=2
    ip=10.1.3.2
    mac=001a64f9bfc9
    mgt=hmc
    nodetype=lpar,osi
    os=AIX
    parent=clstrf1fsp03-9125-F2A-SN024C352
    pprofile=compute
Most of these attributes should have been filled in automatically by xCAT.
Note: xCAT supports many different cluster environments and the attributes that may be required in a node definition will vary. For diskless nodes the node definition should include at least the attributes listed in the above example.
## Initialize the AIX/NIM diskless nodes

You can set up NIM to support a diskless boot of nodes by using the xCAT mkdsklsnode command. This command uses information from the xCAT database and default values to run the appropriate NIM commands.

For example, to set up all the nodes in the group “aixnodes” to boot using the SPOT (COSI) named “61cosi” you could issue the following command.

mkdsklsnode -i 61cosi aixnodes

  The command will define and initialize the NIM machines. It will also set the “provmethod” attribute in the xCAT node definitions to “61cosi “.
Starting with xCAT version 2.5 you can also to specify the “configdump” attribute to specify the type of system do to configure. See the section called “ISCSI dump support” below for details.
To verify that NIM has allocated the required resources for a node and that the node is ready for a network boot you can run the “lsnim –l” command. For example, to check node “node01” you could run the following command.
lsnim -l node01
## Verifying the node initialization before booting (optional)
Once the mkdsklsnode command completes you can check several things to see if it has been initialized correctly.
- The /etc/bootptab and /etc/exports files.
- The <nodename>.info file in the /tftpboot directory.
- The NIM node definition for the node. (“lsnim -l node01”)
## Open a remote console (optional)
You can open a remote console to monitor the boot progress using the xCAT rcons command. This command requires that you have conserver installed and configured.
If you wish to monitor a network installation you must run rcons before initiating a network boot.
To configure conserver run:
makeconservercf
To start a console:
rcons node01
Note: You must always run makeconservercf after you define new cluster nodes.
## Initiate a network boot
Initiate a remote network boot request using the xCAT rnetboot command. For example, to initiate a network boot of all nodes in the group “aixnodes” you could issue the following command.
rnetboot aixnodes
Starting with xCAT version 2.5 you can also specify the “-I” option to specify the iscsi boot option. (“rnetboot -I aixnodes”) See the section called “ISCSI dump support” below for details.
Note: If you receive timeout errors from the rnetboot command, you may need to increase the default 60-second timeout to a larger value by setting ppctimeout in the site table:
chdef -t site -o clustersite ppctimeout=180
## Verify the deployment
- You can use the AIX lsnim command to see the state of the NIM installation for a particular node, by running the following command on the NIM master:
  lsnim -l <clientname>
- Retry and troubleshooting tips:
- For p6 lpars, it may be helpful to bring up the HMC web interface in a browser and watch the lpar status and reference codes as the node boots.
- Verify network connections
- If the rnetboot returns “unsuccessful” for a node, verify that bootp and tftp is configured and running properly.
- For bootp, view /etc/bootptab to make sure an entry exists for the node.
- For dhcp, view /var/lib/dhcp/db/dhcpd.leases to make sure an entry exists for the node.
- Verify that the information in /tftpboot/<node>.info is correct.
- Stop and restart inetd:
stopsrc -s inetd
startsrc -s inetd
Stop and restart tftp:
stopsrc -s tftp
startsrc -s tftp
- Verify NFS is running properly and mounts can be performed with this NFS server:
- View /etc/exports for correct mount information.
- Run the showmount and exportfs commands.
- Stop and restart the NFS and related daemons:
stopsrc -g nfs
startsrc -g nfs
- Attempt to mount a file system from another system on the network.
- If the rnetboot operation is successful, but lsnim shows that the node is stuck at one of the netboot phases, you may need to redo your NIM definitions.
# ISCSI dump support
Starting with xCAT version 2.5.1 you can configure remote system dump support for diskless nodes. To set up the diskless dump support you must define the NIM dump resource and allocate the resource to the diskless node.
When a dump resource is allocated to a client node, NIM creates a subdirectory identified by the client's name for the client's exclusive use. The client uses this directory to store any dump files it creates. For example, “/install/nim/dump/61dskls_dump/node05”.
See the AIX/NIM documentation for more information on the diskless (thin server) dump support.
## Prerequisites
The xCAT support for diskless system dump has the following prerequisites.
- xCAT version 2.5.1 or higher
- Hardware: POWER6 or later
- Operating system version: AIX 6.1.6 or above
- Required firmware: pfw350
- Software prereqs:
- devices.tmiscw (Latest available from the AIX Expansion Pack)
- bos.rte.serv_aid ( version 7.1.0.2 or 6.1.6.2 or later)
- bos.sysmgt.nim.spot (version 7.1.0.1 or 6.1.6.1 or later)
## Configuring diskless dump
The process for configuring xCAT diskless dump support is provided below. These additional steps should be integrated into the AIX diskless deployment process described above.
Install prerequisite software

The devices.tmiscw, bos.rte.serv_aid and bos.sysmgt.nim.spot filesets must be installed on the xCAT management node and service nodes.

The bos.rte.serv_aid and bos.sysmgt.nim.spot filesets must also be installed in the SPOT resource being used for the diskless node.

Use the standard AIX interfaces to install the software on the management node. (SMIT, installp, geninstall)

For the service nodes you can add the filesets to the service node installp_bundle resource you use to install the service node. (ex. xCATaixSN71.) The filesets can be included when you do the initial installation or they can be installed later with the updatenode command.

To install the bos.rte.serv_aid and bos.sysmgt.nim.spot in the SPOT resource you can use either the xcatchroot command to run the installp command on the SPOT, or you can use the mknimimage -u command. (See the man pages for the commands for details.)

To use the mknimimage command you should first update the NIM installp_bundle resource you are using for your diskless osimage. (ex. xCATaixCN71)

To see what software has been installed in the SPOT you can run:

nim -o showres 61spot

Once you are done updating the SPOT you must always run the NIM “check” operation.
nim -Fo check 61spot

Create a NIM dump resource
If you are creating a new diskless osimage then you can have the dump resource created automatically when you run mknimimage. See the mknimimage man page for more details.

For example,

mknimimage -V -r -D -t diskless -s 61rte_lpp_source
61dskls max_dumps=1

The “-D” option specifies that a dump resource should be created.

When creating a dump resource there are several dump-related attributes that may be set.

dumpsize - The maximum size for a single dump image the dump resource will accept. Space is not allocated until a client starts to dump. The default size is 50GB. The dump resource should be large enough to hold the expected AIX dump and snap data.

max_dumps	- The maximum number of dumps that can be collected for a client node. For example, if max_dumps is 2, you can save 2 dumps for the client. If 2 dumps have been saved and a new dump is taken, the oldest one is overwritten. The default is one.

notify - An administrator supplied script that will be invoked when a new dump is captured, or when a dump error occurs on the client. No default value.

snapcollect - Indicates whether snap data should be included with the dump. The snap data file will be saved in the client's dump resource directory. Values are "yes" or "no". The default is "no".

If you already have created a diskless osimage then you can just create the
NIM dump resource manually and add the name to the xCAT osimage definition.

To create a NIM dump resource you could run a command similar to the following (or use SMIT):

nim -o define -t dump -a server=master -a	location=/install/nim/61dskls_dump
-a max_dumps=1 61dskls_dump

To add this to the 61dskls osimage definition you could run the following:

chdef -t osimage -o 61dskls dump=61dskls_dump

Initialize the diskless client node
Use the xCAT mkdsklsnode command to define and initialize a NIM diskless machine.

For example:

mkdsklsnode -V -i 61dskls compute15 configdump=full

When initializing a node there are two dump-related attributes that may be set.

dump_iscsi_port - The tcpip port number to use to communicate dump images from the client to the dump resource server. Normally set by default. This port number is used by a dump resource server.

configdump - Specifies the type of dump to be collected from the client node. The values are "selective", "full", and "none". If the configdump attribute is set to "full" or "selective" the client will automatically be setup to dump to an iSCSI Target device. The "selective" memory dump will avoid dumping user data. The "full" memory dump will dump all the memory of the client partition. Selective and full memory dumps will be collected in the dump resource allocated to the client. Setting the value to “none” means that the dump configuration will not be done on the node. The default value is “selective”.

Warning: Part of the initialization process is to allocate the NIM dump resource to the node. If the node has previously used this dump resource to store any dump files the files will be removed. It is adviseable to copy any dump files you want to keep to a different location so they are not accidently removed.

Boot the node
Use the xCAT rnetboot command to boot the diskless node.

rnetboot compute15
1. Verify that the dump device has been configured on the node. (optional)

Log on to the node or use xdsh to run the AIX sysdumpdev command.

sysdumpdev

The result should be something like the following.

primary /dev/hdisk0
secondary /dev/sysdumpnull
copy directory /var/adm/ras
forced copy flag TRUE
always allow dump FALSE
dump compression ON
type of dump fw-assisted
full memory dump disallow

## Initiating a diskless dump
System dumps are normally initiated when a fatal system error occurs, however, you
can also initiate a system dump using the AIX sysdumpstart command.

For example, to initiate a system dump on a diskless node called "compute15"
you could run the following:

xdsh compute15 "sysdumpstart -p"

The time for the dump to complete will vary depending on the dump options you specify and your network performance etc., however, it could take 2 or more hours to complete in some cases.

When you initiate a dump with the sysdumpstart command the node will be unavailable for the duration of the dump process. The node will automatically reboot after the dump completes.

If you wish to monitor the dump progress you can open a console for the node using the the rcons command. When you see the node rebooted you know the dump should be done. Once the node is rebooted you could also run the “sysdumpdev -L” command on the node to find out if the dump was successful.

The dump file will be created in the NIM dump resource subdirectory created for the node on it's NIM master. The NIM master for the node will either be the xCAT managemant node or a service node. If the dump file is on a service node you must either copy it to the management node or log on to the service node to debug it.

If the snapcollect attribute was set to “no” (which is the default) then you should get a dump file with a name something like “dump.<date>.BZ”

For example,
“/install/nim/dump/61dskls_dump/clstrn05/dump.2010.06.15.10:47:34.BZ”.

If the snapcollect attribute was set to “yes” then you will see a snap file with a name similar to “ snap.pax.<date>.Z” In this case you must extract the dump file from the snap file.

Use the following process to extract the dump file.
1. Uncompress the snap file
  uncompress snap.pax.2010.11.09.15:53:04.Z
2. Get the name of the dump file contained in the snap file

pax -v -f snap.pax.2010.11.09.15:53:04 | grep BZ

Create a subdirectory to save the dump file (ex. /install/nim/dump/710dskls_dump/compute04/savedump)

mkdir savedump

Copy the snap file to the subdirectory

cp snap.pax. 2010.11.09.15:53:04 savedump

Extract the dump file

cd savedump
pax -rvf snap.pax.2010.11.09.15:53:04 -x pax ./dump/dump.2010.11.09.15:52:25.BZ

(ex. /install/nim/dump/710dskls_dump/compute04/savedump/dump/dump.2010.11.09.15:52:25.BZ)

Note: You may need to run “ulimit -f unlimited” command to set the file size limit.

Once you have the dump.<date>.BZ file you can uncompress it using the AIX dmpuncompress command. For example:

dmpuncompress dump.2010.11.09.15:52:25.BZ

The AIX dmpuncompress command restores the original dump files that were compressed at dump time. The compressed dump file is removed and replaced by an expanded copy. The expanded file has the same name as the compressed version, but without the .BZ
## NIM snap and showdump operations

You must run nim commands on the NIM master that is being used for the node. In an xCAT cluster this would either be the management node or an AIX service node. You can use the xCAT xdsh command to run the nim command on the service nodes.

For example, to run the NIM command on the xCAT service node named “SN27”.

xdsh SN27 “<nim command>”
### Snap operation

The NIM “snap” operation allows you to gather system configuration data from a node at any time without having to initiate a system dump. ("nim –o snap –a snap_flags=<value> nodename") The default value for “snap_flags” is “-a” which means it gathers all system configuration information. See the AIX documentation for details on the AIX snap command usage and the “nim -o snap” operation.

For example:
nim –o snap compute15

The snap file (ex. snap.pax.2010.02.17.11:47:38.Z) will be saved in the dump
resource directory. If the snap operation is run again it will remove the existing snap file.

### Showdump operation

Use the NIM "showdump" operation to see what dump files are available for a node.

To run the command on the management node.

nim -o showdump compute15

## Reading a system dump file
Use the AIX kdb command to read dump files.

For example, after you have run the dmpuncompress command you could run the following:

kdb ./dump.2010.11.09.15:52:25 ./unix_64

The “unix_64” should be the one contained in the corresponding SPOT (ex. “/install/nim/spot/<spotname>/usr/lib/boot/unix_64”)

If kdb does not work correctly you should check the build levels of the unix_64 and dump file. If they do not match then kdb will not work.

To check the build levels you could run the following commands.

what unix_64 | grep unix

what dump.2010.11.09.15:52:25 | grep buildinfo

If the levels do not match then you should check to make sure the correct prerequisite software levels have been installed and then try running the “nim -Fo check” operation on the SPOT. You will have to shut the nodes down and run rmdsklsnode before updating the SPOT resource.

See the kdb documentation for more details on how to use kdb with dump files.

# Special Cases
## Using other NIM resources.
When you run the mknimimage command to create a new xCAT osimage definition it will create default NIM resources and add their names to the osimage definition. It is also possible to specify additional or different NIM resources to use for the osimage. To do this you can use the “attr=val [attr=val ...]” option. These “attribute equals value” pairs are used to specify NIM resource types and names to use when creating the the xCAT osimage definition. The “attr” must be a NIM resource type and the “val” must be the name of a previously defined NIM resource of that type, (ie. "<nim_resource_type>=<resource_name>").
For example, to create a diskless image and include tmp and home resources you could issue the command as follows. This assumes that the mytmp and myhome NIM resources have already been created by using NIM commands directly.
        mknimimage -t diskless -s /dev/cd0 611cosi tmp=mytmp home=myhome
These resources will be added to the xCAT osimage definition. When you initialize a node using this definition the mkdsklsnode command will include all the resources when running the “nim -o dkls_init” operation.
See the NIM documentation for more information on supported diskless resources.
## Booting a “dataless” node.
AIX NIM includes support for “dataless” systems as well as “diskless”. NIM defines a dataless machine as one that has some local disk space that could be used for paging space and optionally the /tmp and /home. If you wish to use dataless machines you can create an xCAT osimage definition for them with the mknimimage command. When creating the osimage, use the “-t” option to specify a type of “dataless”.

For example, to create an osimage definition for “dataless” nodes you could run the command as follows.

mknimimage -s /dev/cd0 -t dataless 53cosi

When the node is initialized to use this image the mkdsklsnode command will run the “nim -o dtls_init ..” operation.

See the NIM documentation for more information on the NIM support for dataless systems.
## Specifying additional values for the NIM node initialization.
When you run the mkdsklsnode command to initialize diskless nodes the command will run the required NIM commands using some default values. If you wish to use different values you can specify them on the mkdsklsnode command line using the “attr=val [attr=val ...]” option. See the mkdsklsnode man page for the details of what attributes and values are supported.
For example, when mkdsklsnode defines the diskless node there are default values set for the “speed”(100) and “duplex”(full) network settings. If you wish to specify a different value for “speed” you could run the command as follows.
mkdsklsnode -i myosimage mynode speed=1000
# Cleanup
The NIM definitions and resources that are created by xCAT commands are not automatically removed. It is therefore up to the system administrator to do some clean up of unused NIM definitions and resources from time to time. (The NIM lpp_source and SPOT resources are quite large.) There are xCAT commands that can be used to assist in this process.
## Removing NIM machine definitions
Use the xCAT rmdsklsnode command to remove all NIM machine definitions that were created for the specified xCAT nodes. This command will not remove the xCAT node definitions.

For example, to remove the NIM machine definition corresponding to the xCAT node named “node01” you could run the command as follows.

rmdsklsnode node01

The previous example assumes that the NIM machine definition is the same name as the xCAT node name. If you had used the “-n” option when you created the NIM machine definitions with mkdsklsnode then the NIM machine names would be a combination of the xCAT node name and the osimage name used to initialize the NIM machine. To remove these definitions you must provide the rmdsklsnode command with the name of the osimage that was used.

For example, to remove the NIM machine definition associated with the xCAT node named “node2” and the osimage named “61spot” you could run the following command.

rmdsklsnode -i 61spot node02

If the NIM machine is currently running or the machine definition was left in a bad state you can use the rmdsklsnode “-f” (force) option. This will stop the node and deallocate any resources it is using so the machine definition can be removed.

The rmdsklsnode command is intended to make it easier to clean up NIM machine definitions that were created by xCAT. You can also use the AIX nim command directly. See the AIX/NIM documentation for details.

## Removing NIM resources
Use the xCAT rmnimimage command to remove all the NIM resources associated with a given xCAT osimage definition. The command will only remove a NIM resource if it is not allocated to a node. You should always clean up the NIM node definitions before attempting to remove the NIM resources. The command will also remove the xCAT osimage definition that is specified on the command line.
For example, to remove the “61spot” osimage definition along with all the associated NIM resources run the following command.
rmnimimage -x 61spot
If necessary, you can also remove the NIM definitions directly by using NIM commands. See the AIX/NIM documentation for details.
# Notes
## Terminology
image
The term “image” is used extensively in this document. The precise meaning of an “image” will vary depending on the context in which the term is being used. In general you can think of an image as the basic operating system image as well as other resources etc. that are needed to boot a node. In most cases in this document we will be referring to an image as either an xCAT osimage definition or an AIX/NIM diskless image (called a SPOT or COSI).

osimage - This is an xCAT object that can be used to describe an operation system image. This definition can contain various types of information depending on what will be installed on the node and how it will be installed. The image definition is not node specific and can be used to deploy multiple nodes. It contains all the information that will be needed by the underlying xCAT and NIM support to deploy the node.

COSI - A Common Operating System Image is the name used by AIX/NIM to refer to a SPOT resource. From the NIM perspective this would be an AIX diskless image.

diskless node
The operating system is not stored on local disk. For AIX systems this means the file systems are mounted from a NIM server. NIM also supports the concept of a dataless system which has some limited disk space that can be used for certain file systems. See the “Special Cases” section below for information on using additional NIM features.

diskful node
For AIX systems this means that the node has local disk storage that is used for the operating system. Diskfull AIX nodes are typically installed using the NIM rte or mksysb type install methods.

## NIM diskless resources
The following list describes the required and optional resources that are managed by NIM to support diskless and dataless clients.

boot
Defined as a network boot image for NIM clients. The boot resource is managed automatically by NIM and is never explicitly allocated or deallocated by users.
SPOT
Defined as a directory structure that contains the AIX run-time files common to all machines. These files are referred to as the usr parts of the fileset. The SPOT resource is mounted as the /usr file system on diskless and dataless clients.
Contains the root parts of filesets. The root part of a fileset is the set of files that may be used to configure the software for a particular machine. These root files are stored in special directories in the SPOT, and they are used to populate the root directories of diskless and dataless clients during initialization.
The network boot images used to boot clients are constructed from software installed in the SPOT.
A SPOT resource is required for both diskless and dataless clients.
root
Defined as a parent directory for client "/" (root) directories. The client root directory in the root resource is mounted as the "/" (root) file system on the client.
When the resources for a client are initialized, the client root directory is populated with configuration files. These configuration files are copied from the SPOT resource that has been allocated to the same machine.
A root resource is required for both diskless and dataless clients.
This resource is managed automatically by NIM.
dump
Defined as a parent directory for client dump files. The client dump file in the dump resource is mounted as the dump device for the client.
A dump resource is required for both diskless and dataless clients.
This resource is managed automatically by NIM.
paging
Defined as a parent directory for client paging files. The client paging file in the paging resource is mounted as the paging device for the client.
A paging resource is required for diskless clients and optional for dataless clients.
This resource is managed automatically by NIM.
home
Defined as a parent directory for client /home directories. The client directory in the home resource is mounted as the /home file system on the client.
A home resource is optional for both diskless and dataless clients.
shared_home
Defined as a /home directory shared by clients. All clients that use a shared_home resource will mount the same directory as the /home file system.
A shared_home resource is optional for both diskless and dataless clients.
tmp
Defined as a parent directory for client /tmp directories. The client directory in the tmp resource is mounted as the /tmp file system on the client.
A tmp resource is optional for both diskless and dataless clients.
resolv_conf
This resource is a file that contains nameserver IP addresses and a network domain name.
It is copied to the /etc/resolv.conf file in the client's root directory.
A resolv_conf resource is optional for both diskless and dataless clients.
The AIX/NIM resources for diskless/dataless machines will remain allocated and the node will remain initialized until they are specifically unallocated and uninitialized.

## NIM Commands
### COSI commands
AIX provides commands that may be used to manage the SPOT (or COSI) resource. Refer to the AIX man pages for further details.
- mkcosi Create a COSI (SPOT) for a thin server (diskless or	dataless client) to mount and use.
- chcosi Manages a Common Operating System Image	(COSI).
- cpcosi Create a copy of a COSI (SPOT).
- lscosi List the properties of a COSI (SPOT).
- rmcosi Remove a COSI (SPOT) from the NIM environment.
### Thin server commands
AIX provides several commands that can be used to manage diskless (also called thin server) nodes. See the AIX man pages for further details.
- mkts Create a thin server and all necessary resources.
- lsts List the status and software content of a thin server.
- swts Switch a thin server to a different COSI.
- dbts Perform a debug boot on a thin server.
- rmts Remove a thin server from the NIM environment.